## Slide 1: Register Cache System not for Latency Reduction Purpose
Ryota Shioya, Kazuo Horio,
Masahiro Goshima, and Shuichi Sakai
The University of Tokyo
Notes: Thank you chairman.
(My name is Ryota Shioya.
Today I would like to talk about Register Cache System not for Latency Reduction Purpose.

## Slide 2: Outline of research
The area of register files of OoO superscalar processors has been increasing
  It is comparable to that of an L1 data cache
  A large RF causes many problems
    Area, complexity, latency, energy, and heat …
A register cache was proposed to solve these problems
  But … miss penalties most likely degrade IPC
We solve the problems with a “not fast” register cache
  Our method is faster than methods with a “fast” register caches
  Circuit area is reduced to 24.9% with only 2.1% IPC degradation
Notes: This is an outline of today’s presentation.
Recently, the area of register files of OoO superscalar processors has been increasing.
And it is comparable to that of L1 data cache.
  A large RF causes many problems.
Especially, energy consumption and heat are serious.
A register cache was proposed to solve these problems of the RF.
But miss penalties most likely degrade IPC.
We solve the problems with a “not fast” register cache
Our method is faster than methods with a “fast” register cache
Our evaluations show a circuit area is reduced to 24.9%, and
IPC degradation is no more than 2.1%

## Slide 3: Background : The increase in the circuit area of register files
The area of register files of OoO superscalar processors has been increasing
  The increase in the number of entries
    The required entry number of RFs is proportional to in-flight instructions
    Multi-threading requires a number of entries that are proportional to the thread number
  The increase in the number of ports
    A register file consists of a highly ported RAM
    The area of a RAM is proportional to the square of the port number
Notes: Now let me introduce the background
Recently, the area of register files of OoO superscalar processor has been increasing.
There are two reasons for this.
That is the increase in entries and ports of RFs.
For achieving high IPC, many entries are required.
Multi-threading also requires many entries.
The second reason is the increase in the number of ports.
A register file consists of a highly ported RAM.
The area of a RAM is proportional to the square of the port number.

## Slide 4: RF area is comparable to that of an L1 data cache Ex: Integer execution core of Pentium4
L1 Data cache
16KB 1 read/1 write
Register file
64 bits 144 entries 6 read/3 write
(double pumped)
（ from http://www.chip-architect.com）
Notes: As a result of the increases, RF area is comparable to that of an L1 data cache.
This is a photograph of an integer execution core of a Pentium4.
The left yellow rectangles are L1 data caches.
The right red rectangles are register files.
This photograph shows these areas are almost the same.
//This holds true for more recent processor cores

## Slide 5: Problems of large register files
The increase of energy consumption and heat from it
  The energy consumption of a RAM is proportional to its area
  A region including a RF is a hot spot in a core
    It limits clock frequency
The increase in access latency
  Access latency of a RF is also comparable to that of an L1D$
  A RF is pipelined
    The increase in bypass network complexity
    A deeper pipeline decreases IPC
      Prediction miss penalties
      Stalling due to resource shortage
Notes: A large register file causes many problems.
These two problems are important.
First, energy consumption and heat from it.
The energy consumption of a RAM is proportional to its area.
A region including a RF is a hot spot of a core,
So it limit the clock frequency
Second, the increase in access latency
  Access latency of a RF is also comparable to that of L1D$
So, a RF is pipelined similar to L1D$.
    Pipelining a RF leads to the increase in bypass network complexity
    And a deeper pipeline usually decrease IPC.

## Slide 6: Register cache
proposed to solve the problems of a large RF
Register cache（RC）
  A small & fast buffer
  It caches values in a main register file（MRF）
Miss penalties of a RC most likely degrade IPC
  Ex. It degrades IPC by 20.9% ( 8 entry RC system )
Notes: A register cache is proposed to solve these problems of a large RF.
The RC is a small and fast buffer and it caches values in the main register file.
However, miss penalties of a RC most likely degrade IPC.
For example, our evaluations show that IPC degradation by RC misses is 20.9%.

## Slide 7: Our proposal
Research goal :
  Reducing the circuit area of a RF
We achieve this with a “not fast” register cache
  Our RC does not reduce latency
  Our method is faster than methods with “fast” register caches
Notes:   Our goal of the research is to reduce the circuit area of a register file.
We achieve this with a “not fast” register cache.
Our RC does not reduce latency,
but it is faster than methods with “fast” register caches.
Our Evaluation results shows that the circuit area is reduced to 24.9%, and
IPC degradation is no more than 2.1%
  Shifts RC miss penalties to branch miss prediction penalties

## Slide 8: Our proposal
Usually, the definition of a cache is “cache is a fast one”
  Text books
  Wikipedia
  You may think …
  In this definition
    Our proposal is not a cache
One may think …
  Why a RC that does not reduce latency works
    A not fast cache is usually meaningless
  Why a not fast cache overcomes a fast cache
Notes: Usually, the definition of a cache is “cache is a fast one”.
I found this in some text books and wikipedia.
And you may think so too.
In this definition, our proposal is not a cache.
One may think,
Why a RC that does not reduce latency works?
A not fast cache is usually meaningless
  Why a not fast cache overcomes a fast cache?
  In the following , I will talk about them.

## Slide 9: Outline
Conventional method : LORCS : Latency-Oriented Register Cache System
Our proposal： NORCS : Non-latency-Oriented Register Cache System
Details of NORCS
Evaluation
Notes: This is the outline of the following section.
First, I will talk about LORCS. This is a conventional method that solves the problems of a large RF.
The second topic is NORCS. This is our proposal.
Then, I will talk about detailed topics about NORCS.
Finally, I will show evaluations of systems.

## Slide 10: Register cache
Register cache (RC)
  A RC is a small and fast buffer
  caches values in the main register file（MRF）
Notes: A RC is a small and fast buffer
and it caches values in the main register file.

## Slide 11: Register cache system
A register cache system refers to a system that includes the followings :
    Register cache
    Main register file
    Pipeline stages
Register cache
Instruction
Window
Write Buffer
Main Register File
ALUs
Out of pipelines
Notes: A register cache system refers to a system that includes the followings.
A register cache, A main register file, and pipeline stages.
Note that a MRF is placed out of pipelines, it is accessed only on RC miss.

## Slide 12: LORCS : Latency-Oriented-Register Cache System
Two different register cache system
  Latency-Oriented : Conventional method
  Non-Latency-Oriented : Our proposal
LORCS : Latency-Oriented-Register Cache System
  A conventional RC system is referred to as it in order to distinguish it from our proposal
  Usually, the “Register Cache” refers this
Notes: I will talk about two different register cache systems.
latency oriented one, it is a conventional method
non-latency oriented one, it is our proposal
A conventional RC system is Latency-Oriented-Register Cache System, we call it LORCS.
We call so in order to distinguish from our proposal.
Usually the RC refers this.

## Slide 13: LORCS : Latency-Oriented-Register Cache System
Pipeline that assumes hit
  All instructions are scheduled assuming their operands will hit
  If all operands hit,
    It is equivalent to a system with a 1-cycle latency RF
  On the RC miss, pipeline is stalled (miss penalty)
  This pipeline is the same as a general data cache
Notes: LORCS has a pipeline that assumes hit.
In LORCS, All instructions are scheduled assuming their operands will hit
If all operands hits , LORCS is equivalent to a system with a one cycle latency RF.
On the RC miss, pipeline is stalled.
This pipeline is the same as a general data cache.

## Slide 14: Behavior of LORCS
  On RC miss, the processor backend is stalled
  MRF is accessed in the meantime
cycle
I1 :
I2 :
I3 :
I4 :
I5 :
IS
CR
CR
EX
IS
CR
CR
IS
CW
EX
CW
CR
CR
EX
CW
IS
CR
CR
EX
CW
IS
CR
CR
EX
CW
RR
RR
Miss
Stall
CR | RC Read
CW | RC Write
RR | MRF Read
CR
CW
RR
Notes: This figure shows behavior of the LORCS
IS is instruction issue, CR is RC read, EX is execution, CW is RC write.
The CR and RR stages are horizontally divided into 2.
It represents two source operands.
When all operands hit a RC, instructions are executed in this way.
This is equivalent to behavior of a 1 cycle latency register file.
Next, I will talk about behavior on miss.
The cycle time is progressed, and now an operand of instruction I2 missed the RC.
The processor backend is stalled and a MRF is accessed in the meantime.
This is a miss penalty.

## Slide 15: Consideration of RC miss penalties
  The processor backend is stalled on RC misses
  OoO superscalar processors can selectively delay instructions with long latency
  One may think that the same can be used for RC misses
Selective delay of instructions on RC misses is difficult
  Non-re-schedulability of a pipeline
Notes:   The processor backend is stalled on RC misses
  Usually, OoO superscalar processors can selectively delay instructions with long latency
One may think that the same can be done on RC misses.
However, selective delay of instructions on RC misses is difficult
  This is because of Non-re-schedulability of a pipeline.

## Slide 16: Non-re-schedulability of a pipeline
Instructions cannot be re-scheduled in pipelines
Register cache
Instruction Window
Write Buffer
Main Register File
ALUs
I0
I1
I2
I3
I4
I5
I0 misses RC
Out of pipelines
Notes: I will talk about this by using this figure.
This is a backend pipeline of LORCS.
Now I0 and I1 are issued from the instruction window.
…
I0 misses the RC.
At this timing, if you want to delay I0 selectively,
on the next cycle, there is no place for the following I2.
Moreover, if I3 depends on I0,
I3 must be delayed and the processor must detect this.
This means an additional scheduling logic and instruction window are required here,
If you want to delay instructions selectively.
But it is unrealistic.

## Slide 17: Purposes of LORCS
Reducing latency：
  In the ideal case, it can solve all the problems of pipelined RFs
    Reducing prediction miss penalties
    Releasing resources earlier
    Simplifies bypass network
Reducing ports of a MRF
Notes: purposes of the LORCS are reducing latency and reducing ports of a MRF.
First, In the ideal case, it can solve all the problems of pipelined RFs.
It reduces prediction miss penalty,
releases resources earlier,
simplify bypass network.

## Slide 18: Reducing ports of a MRF
Only operands that caused RC misses access MRF
  requires only a few ports
Reducing the area of the MRF
  RAM area is proportional to the square of the port number
ALUs
Register cache
Main Register file
ALUs
Register file
Notes: Second, it can reduce the ports of a MRF.
Only operands that caused RC misses access a MRF,
Therefore a MRF has a few ports.
The area of a RAM is proportional to the square of the port number,
So it reduces the area of the MRF greatly.

## Slide 19: Outline
Conventional method : LORCS : Latency-Oriented Register Cache System
Our proposal： NORCS : Non-latency-Oriented Register Cache System
Details of NORCS
Evaluation
Notes: Next, I talk about our proposal NORCS.

## Slide 20: NORCS : Non-latency-Oriented Register Cache System
NORCS also consists of
  RC, MRF, and Pipeline stages
It has a similar structure to LORCS
  It can reduce the area of a MRF by a similar way of LORCS
  NORCS is much faster than LORCS
Important difference
  NORCS has stages accessing a MRF
Notes: NORCS : Non-latency-Oriented Register Cache System
also consists of a RC, a MRF, and pipeline stages.
It has a similar structure to LORCS.
and it can reduce the area of a MRF by a similar way of LORCS.
Hwevere, NORCS is much faster than LORCS
  An important difference is that NORCS has stages accessing a MRF.

## Slide 21: NORCS has stages accessing the MRF
RC
MRF
ALUs
RC
MRF
ALUs
IW
IW
LORCS:
NORCS:
The difference is quite small, but it makes a great difference to the performance
Out of pipelines
Notes: These figures show block diagrams of LORCS and NORCS.
The upper half is LORCS
The lower half is NORCS, our proposal
Both consist of a RC, a MRF, and pipelines.
An important difference is that NORCS has stages accessing the MRF,
But LORCS doesn’t have them.
The MRF is placed out of the pipelines.
The difference in the logic is quite small,
but it makes a great difference to the performance

## Slide 22: Pipeline of NORCS
NORCS has stages to access the MRF
Pipeline that assumes miss：
  All instructions wait as if it had missed regardless of hit / miss
It is a cache, but
  does not make processor fast
Notes: NORCS has stages to access the MRF,
which means that
NORCS has a pipeline that assumes a RC miss.
All instructions wait as if it had missed regardless of hit /miss.
So, it is a cache, but it does not make processor fast.

## Slide 23: Pipeline that assumes miss
CR
CR
Pipeline of NORCS is not stalled only on RC misses
The pipeline is stalled when the ports of the MRF are short.
IS
EX
CW
cycle
RR
RR
RR
RR
CR
CR
IS
EX
CW
RR
RR
RR
RR
CR
CR
IS
EX
CW
RR
RR
RR
RR
CR
CR
IS
EX
CW
RR
RR
RR
RR
RC hit
RC hit
RR
RR
：does not access MRF
：accesses MRF
RR
I1 :
I2 :
I3 :
I4 :
I5 :
CR
CR
IS
EX
CW
RR
RR
RR
RR
RC hit
RC miss
CR | RC Read
CW | RC Write
RR | MRF Read
CR
CW
RR
Notes: This is behavior of NORCS.
All the operands of I1 hit the RC.
on the following stages, the operands do not access the MRF.
When one of the operands of the I2 misses the register cache,
on the following stages, the operand accesses the MRF.
All the operands of I3 and I4 hit the RC.
Their operands don’t access the MRF.
This figure shows the pipeline of NORCS is not stalled only on the RC misses.
The pipeline is stalled when the ports of the MRF are short.

## Slide 24: Pipeline disturbance
Conditions of pipeline stalls :
  LORCS :
    If one ore more register cache misses occur at a single cycle
  NORCS:
    If RC misses occur more than MRF read ports at a single cycle
      The MRF is accessed in the meantime
    This probability is very small
      Ex. 1.0% in NORCS with 16 entries RC
Notes: Conditions of pipeline stalls are summarized here.
    In LORCS, if one or more register cache misses occur, the pipeline is stalled.
    On the other hand, in NORCS,
    If RC misses occur more than MRF read ports, the pipeline is stalled.
    This probability is very small.
For example, in NORCS with 16 entries RC, this is 1.0%

## Slide 25: Outline
Conventional method : LORCS : Latency-Oriented Register Cache System
Our proposal： NORCS : Non-latency-Oriented Register Cache System
Details of NORCS
  Why NORCS can work
  Why NORCS is faster than LORCS
Evaluation
Notes: Now, I will talk about details of NORCS.
I will talk about
Why NORCS can work and
Why NORCS is faster than LORCS

## Slide 26: Why NORCS can work
A pipeline of NORCS can work only for a RC
  A not fast cache is meaningless in general data caches
Explain this by :
  data flow graph (DFG)
  dependencies
    There are two types of dependencies
      “Value – value” dependency
      “Via – Index” dependency
Notes: A pipeline of NORCS can work only for a RC.
A not fast cache is meaningless in general data caches.
I try to explain this by using
Data flow graph and two types of dependencies.
There are two types of dependencies.
“Value – value” dependency and
“Via – Index” dependency

## Slide 27: Value – value dependency
Data cache
  A dependency from a store to a dependent load instruction
  The increase in the latency possibly heightens the DFG
store [a] ← r1
load r1 ← [a]
Height of DFG
L1
L1
L1
L1
AC
AC
store [a] ← r1
load r1 ← [a]
Height of DFG
L1
L1
L1
L1
L1
L1
AC
AC
Cache Latency
Notes: In a data cache,
A Value – value dependency means a dependency
from a store to a dependent load instruction.
  The increase in the latency possibly heightens the DFG like this.

## Slide 28: Value – value dependency
Register cache
  RC latency is independent of the DFG height
store [a] ← r1
load r1 ← [a]
Height of DFG
mov r1 ← A
add r2 ← r1 + B
Height of DFG
CW
CW
CW
CR
CR
CR
EX
EX
L1
L1
L1
L1
L1
L1
AC
AC
Bypass net can pass the data
Data cache
Notes: On the other hand,
In a register cache,
Since the bypass network can immediately pass the data,
the register cache latency is independent of the height of DFG.

## Slide 29: Via index dependency
Data cache
  A dependency from an instruction to a dependent load instruction
  Ex. : Pointer chasing in a linked list
Register cache
  There are no dependencies from execution results to register number
  The RC latency is independent of the height of DFG
load r1 ← [a]
load r2 ← [r1]
Height of DFG
L1
L1
L1
L1
L1
L1
AC
AC
Notes: Next, via index dependency.
In a data cache,
  It means a dependency from an instruction to a dependent load instruction.
  Typical example of this is pointer chasing in a linked list.
  The increase in the cache latency also heightens the DFG
On the other hand,
In a register cache
  There are no dependencies from execution results to register number
  The register cache latency is independent of the height of DFG
This is a reason why the pipeline of NORCS can work only for a RC.

## Slide 30: Why NORCS is faster than LORCS
Why NORCS is faster than LORCS
  NORCS : always waits
  LORCS : waits only when needed
Because :
LORCS suffers from RC miss penalties with high probability
  Stalls occur more frequently than RC miss of each operand
NORCS can avoid these penalties
  Can shift RC miss penalties to branch miss prediction penalties with low probability
Notes: The second topic is
Why NORCS is faster than LORCS.
NORCS always waits, but LORCS waits only when needed.
Howevere, NORCS is faster than LORCS.
This is because
LORCS suffers from RC miss penalties with high probability.
Stalls occur more frequently than RC miss of each operand.
NORCS can avoid these penalties.
NORCS can shift RC miss penalties to branch miss prediction penalties with low probability.
I will talk about these in the following.

## Slide 31: Stalls occur more frequently than RC miss of each operand
In LORCS, a pipeline is stalled when：
  One or more register cache misses occur at a single cycle
Ex.： SPEC CPUINT 2006 456.hmmer / 32 entries RC
  RC miss rate : 5.8% ( = hit rate is 94.2%)
  Source operands per cycle are 2.49
  Probability that all operands hit
    0.9422.49≒0.86
  Probability to stall (any of operands miss)
    1 - 0.9422.49 ≒0.14 (14%)
Our evaluation shows more than 10% IPC degradation in this benchmark
Notes: In LORCS, a pipeline is stalled when：
One or more register cache misses occur at a single cycle
For example, in a case of SPEC CPU INT 2006 456.hmmer,
RC hit rate is 94.2% and 2.49 instructions are issued on average.
In this case
probability that all operands hit is nearly equal to 0.86,
  Which means probability to stall is nearly 14%.
  This is much larger than bare miss rate.
Our evaluation actually shows more than 10% IPC degradation in this benchmark.

## Slide 32: NORCS can shift those RC miss penalties to branch miss prediction penalties.
•••
•••
EX
IS
•••
IF
IF
penaltybpred
cycle
EX
IF
EX
RR1
RR2
IF
EX
IS
IS
IS
IF
EX
IS
EX
IS
IF
IF
penaltybpred + latencyMRF
EX
IF
EX
IS
IS
latencyMRF
IF
EX
IS
IF
EX
IS
CR
CR
CR
CR
CR
CR
CR
CR
CR
CR
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
CR
CR
CR
CR
CR
CR
CR
CR
CR
CR
I4:
I2:
I1:
I3:
I5:
I4:
I2:
I1:
I3:
I5:
LORCS
NORCS
•••
•••
•••
•••
•••
•••
•••
latencyMRF
Notes: NORCS can shift those RC miss penalties to branch miss prediction penalties.
This is the pipeline diagrams of LORCS and NORCS.
The upper half is behavior of LORCS
and the lower half is behavior of NORCS.
In LORCS,
The left shaded part shows branch miss prediction penalty,
And the right shaded part shows the latency of the MRF, which is RC miss penalty.
In NORCS,
The left shaded part also shows branch miss prediction penalty,
that is longer than that of LORCS by the latency of the MRF.
These figures shows RC miss penalty shifts to branch miss prediction penalty.

## Slide 33: NORCS can shift those RC miss penalties to branch miss prediction penalties.
•••
•••
EX
IS
•••
IF
IF
penaltybpred
cycle
EX
IF
EX
RR1
RR2
IF
EX
IS
IS
IS
IF
EX
IS
EX
IS
IF
IF
penaltybpred + latencyMRF
EX
IF
EX
IS
IS
latencyMRF
IF
EX
IS
IF
EX
IS
CR
CR
CR
CR
CR
CR
CR
CR
CR
CR
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
RR1
RR2
CR
CR
CR
CR
CR
CR
CR
CR
CR
CR
I4:
I2:
I1:
I3:
I5:
I4:
I2:
I1:
I3:
I5:
LORCS
NORCS
•••
•••
•••
•••
•••
•••
•••
latencyMRF
5% 14%
Notes: Usually, probability of RC miss penalty is much higher than that of branch miss prediction penalty.
In the previous example, that of the RC miss penalty is 14%,
and that of branch miss penalty is 5%.
In such a case, NORCS is faster than LORCS.
This is a reason why NORCS is faster than LORCS.

## Slide 34: Outline
Conventional method : LORCS : Latency-Oriented Register Cache System
Our proposal： NORCS : Non-latency-Oriented Register Cache System
Details of NORCS
Evaluation
Notes: Finally, I will show evaluations of the systems.

## Slide 35: Evaluation environment
IPC：
  Using “Onikiri2” simulator
    Cycle accurate processor simulator
    developed in our laboratory
Area & energy consumption
  Using CACTI 5.3
    ITRS 45nm technology node
  Evaluate arrays of RC & MRF
Benchmark ：
  All 29 programs of SPEC CPU 2006
  compiled using gcc 4.2.2 with –O3
Notes: We evaluated IPC, area and energy consumption of the models described before.
We evaluated IPC using Onikiri2 simulator developed in our laboratory.
We evaluated area and energy consumption using CACTI 5.3.
We used all 29 programs of the SPEC CPU 2006 for benchmark.
The programs are compiled using gcc 4.2.2 with –O3

## Slide 36: 3 evaluation models
PRF
  Pipelined RF (Baseline)
  8read/4write ports / 128 entries RF
LORCS
  RC：
    LRU
    Use based replacement policy with a use predictor
      J. A. Butts and G. S. Sohi, “Use-Based Register Caching with Decoupled Indexing,” in Proceedings of the ISCA, 2004,
  2read/2write ports / 128 entries MRF
NORCS
  RC : LRU only
Notes: We evaluated three models.
PRF, LORCS, and NORCS.
PRF is a system with a 8read/4write pipelined RF.
In LORCS, we evaluated RCs with LRU and Use-Based replacement policy proposed by butts and sohi.
The model has a 2read/2write MRF.
In NORCS, we evaluated RCs with LRU only.
the MRF is the same as LORCS

## Slide 37: Simulation Configurations
Configurations are set to match modern processors
Name | Value
fetch width | 4 inst.
instruction window | int：32, fp：16, mem：16
execution unit | int：2, fp：2, mem：2
MRF | int： 128 , fp : 128
BTB | 2K entries, 4way
Branch predictor | g-share 8KB
L1C | 32KB，4way，2 cycles
L2C | 4MB，8way，10 cycles
Main memory | 200 cycles
Notes: These are simulation configurations.
Most parameters are set to modern processor.

## Slide 38: Average probabilities of stalls and branch prediction miss
In NORCS, the probabilities of stalls are very row
In LORCS, the probabilities of stalls are much higher than branch miss penalty in the models with 4,8, and 16 entries RC
Notes: This graph shows probabilities of stalls of each model
and branch prediction misses.
The horizontal axis shows RC entries, and the vertical axis shows probability.
In NORCS, the probabilities of stalls are very row.
In LORCS,
The probability of RC miss penalties are much higher than
Branch miss penalties in the models with 4, 8, and 16 entries.
In these situations, NORCS will be faster than LORCS as described before.

## Slide 39: Average relative IPC All IPCs are normalized by that of PRF
In LORCS, IPC degrades significantly in the models with 4,8,and 16 entries RC
In NORCS, IPC degradation is very small
LORCS with 64 entries LRU RCs and NORCS with a 8 entries RC are almost same IPC …But
Notes: This graph shows average relative IPC.
All IPCs are normalized by that of the PRF model.
In LORCS, IPC degrades significantly in the models with 4,8, and 16 entries RC
In NORCS, IPC degradation is very small.
LORCS with a 64 entries RC and NORCS with a 8 entries RC show almost same
IPCs

## Slide 40: Trade-off between IPC and area RC entries：4, 8, 16, 32, 64
NORCS with 8entries RC :
  Area is reduced by 75.1% with only 2.1% IPC degradation from PRF
Area -75.1%
Notes: This graph shows the relative IPC per circuit areas.
All areas are normalized by that of the PRF model.
Each data point of the line in this figure
indicates a value of the model with a 4-, 8-, 16-, 32-, and
64- entries register cache from left to right.
In NORCS with 8 entries RC,.
The area is reduced by 75.1% with only 2.1% IPC degradation from PRF model.

## Slide 41: Trade-off between IPC and area RC entries：4, 8, 16, 32, 64
NORCS with 8entries RC :
  Area is reduced by 72.4% from that of LORCS-LRU with same IPC
  IPC is improved by 18.7% from that of LORCS-LRU with same area
Area -72.4%
IPC 18.7%
Notes: There is no significant difference of IPCs between
NORCS with 8-entry LRU register cache and LORCS with
64-entry register cache of LRU policy,
However, the area of the model of
NORCS is reduced by 72.4% from the model of LORCS.
NORCS and LORCS with 8 entries LRU register cache show
the same areas. However, the model of
NORCS improves IPC by 18.7% from the model of LORCS.
The models of LORCS USE-B have large areas
Because their use-predictors for replacement are very large.

## Slide 42: Trade-off between IPC and energy consumption RC entries：4, 8, 16, 32, 64
IPC 18.7%
Energy -68.1%
Our proposal（NORCS with 8entries RC ）:
  Energy consumption is reduced by 68.1% with only 2.1% IPC degradation
Notes: This graph shows the relative IPC per energy consumption like the previous graph.
This graph shows the same tendency as that of areas.
  The energy consumption of NORCS is reduced by 68.1% from PRF % with only 2.1% IPC degradation

## Slide 43: Conclusion
A large RF causes many problems
  Especially energy and heat are serious
A register cache was proposed to solve these problems
  Miss penalties degrade IPC
NORCS： Non-latency-Oriented Register Cache System
  We solve the problems with a “not fast” register cache
  Our method overcomes methods with “fast” register caches
  Circuit area is reduced by 75.1% with only 2.1% IPC degradation
Notes: A large RF causes many problems
Area, latency, energy, and heat …
A register cache was proposed to solve these problems
Miss penalties degrade IPC
We solve the problems with a “not fast” register cache
Our method overcomes methods with a “fast” register cache
Evaluations show circuit area is reduced to 24.9% and
IPC degradation is no more than 2.1%

## Slide 44: Appendix

## Slide 46: Onikiri2
Implementation
  Abstract pipeline model for OoO superscalar processor
  Instruction emulation is performed in exec stages
    Incorrect result for incorrect scheduling
Features
  Written in C++
  Support ISA : Alpha and PowerPC
  Can execute all the programs in SPEC 2000/2006
Notes:   Onikiri2 has abstract pipeline model for OoO superscalar processor,
  so it supports any types of OoO superscalar processors.
  Instruction emulation is performed in exec stages.
  Many simulator, such as SimpleScalar and Simics, Instruction emulation is performed in fetch stages.
  Incorrect scheduling cause incorrect result, thus bugs are easily detected.
Onikiri2 is written in C++.
It support Alpha and PowerPC ISA.
  it can execute all the programs in SPEC 2000/2006.

## Slide 47
Arbiter
Register cache
Main register file
Out of instruction pipeline
hit/miss
ALU
Read
reg num
Write
reg num/data
Write
reg num/data

## Slide 48
Data array
Arbiter
Write
buffer
Tag array
Register cache
Main register file
Write data
hit/miss
ALU
Read
reg num
Write
reg num/data
Write
reg num/data
Added latches

## Slide 49: Relative area
80.1%
Notes: This graph shows the circuit areas relative to that of PRF model.
The areas include those of the register
cache, main register file and use-predictor.
In NORCS, the total area of the main register file and the
register cache is reduced to 19.9%, 24.9%, 34.7%,

## Slide 50: Relative energy consumption

## Slide 51: Probabilities of RC miss / penalty / Branch miss