## Slide 1: A Front-end Execution Architecture for High Energy Efficiency
Ryota Shioya*, Masahiro Goshima†, and Hideki Ando*
* Nagoya University
† National Institute of Informatics

## Slide 2: Single thread performance is important even for mobile devices
In smartphones and tablets, major developers have adopted OoO processors
  A high-quality experience is required
  Applications in these devices have become increasingly complex
In fact, iPhone, iPad, and many Android devices are equipped with OoO processors
  e.g. iPhone6: Apple A8 (6-issue OoO processor)
But the energy efficiency is bad

## Slide 3: Heterogeneous Architecture
ARM big.LITTLE consists of the combination of :
  big core（OoO）
  little core (in-order)
It improves energy efficiency by using little cores when high performance is not required
But, when big cores are used, a large amount of energy is still consumed

## Slide 4: Why do OoO processors consume a large amount of energy?
A large amount of energy is consumed by hardware for dynamic instruction scheduling:
  e.g. Issue queue (IQ), load/store queue (LSQ) ...
Such HW comprises heavily multi-ported memories
  A multi-ported memory consumes energy proportionally with the square of the number of the ports
  Consequently, its energy consumption is very large

## Slide 5: Front-end Execution Architecture (FXA)
Goal：
  Improving the energy efficiency of OoO processors
Approach：
  Execute instructions in-order in the processor front-end

## Slide 6: Front-end Execution Architecture (FXA)
FU
Register File
Fetch
Rename
Issue
Queue
FU
FU
Register File
IQ
Fetch
Rename
Conventional
FXA
FU
FU
FU
FU
FU
FU
Issue
Queue
FU
FU
Reduce the FUs in the back-end
Shrink the
issue queue
Add the data-path to the RF and FUs to the front-end

## Slide 7: FXA has two execution units: IXU and OXU
FU
Register File
Fetch
Rename
Issue
Queue
FU
FU
Register File
IQ
Fetch
Rename
Conventional
FXA
FU
FU
FU
FU
FU
OoO Ex. Unit(OXU)
In-order Ex. Unit(IXU)
The IXU executes instructions in-order in the front-end
It functions as a filter for the OXU

## Slide 8: FXA’s merit：improving energy efficiency
IXU：
  The IXU consists of FUs and a bypass network
    The IXU does not include the multi-ported memory
    FUs can be added at low cost, and it improves performance
  The IXU can execute over 50% of all instructions
OXU ：
  The energy-consuming OXU can be shrunk

## Slide 9: Evaluation Results
Compared with ARM Cortex A-57 (big) ,
  FXA achieves:
    5.7% higher IPC
    17% lower energy consumption
    25% improved performance/energy ratio (PER) （PER=the inverse of EDP）
Compared with ARM Cortex A-53 (little)
  FXA achieves 27% improved PER

## Slide 10: Outline
The basic structure and behavior of FXA
Instruction execution in the IXU
Performance and energy consumption
Evaluation

## Slide 11: Basic Structure of FXA
IQ
FU
OXU
IXU
FXA has two execution units:
  1. In-order Ex. Unit (IXU)
    The IXU consists of multiple-staged functional units and a bypass network
  2. Out-of-order Ex. Unit (OXU)
    The OXU is a shrunk OoO back-end
Register File
Fetch
Rename
FU
FU
FU
FU

## Slide 12: Basic Behavior of FXA
IQ
FU
OXU
IXU
Fetched instructions flow through the front-end pipeline inc. the IXU
  Without pipeline stalls, unlike in-order processors
In the IXU, an instruction is ...
  executed where it can be executed, and
  if it cannot be executed in the IXU, it is dispatched to the OXU
The IXU functions as a filter for the OXU
  Instructions executed in the IXU are removed from the pipeline
Register File
Fetch
Rename
FU
FU
FU
FU
I0
I1
I2
I3
I4
I5
I6
I7
I8
I9
I10
I11
I12
I13

## Slide 13: Instructions executed in the IXU
The IXU can execute instructions that get all the source operands in the front-end
The source operands can be got by
  reading the register file in the front-end
  bypassing from instructions executed in the IXU

## Slide 14: Topics
The basic structure and behavior of FXA
Instruction execution in the IXU
  focusing on operand bypassing
Performance and energy consumption
Evaluation

## Slide 15: IXU structure
IXU structure：
  The IXU consists of multiple-staged functional units and a bypass network
  e.g. 2-width x 2-stage IXU
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)

## Slide 16: Instruction execution in the IXU
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
  Describe the behavior of the IXU using the pseudo code
  including the serially dependent instructions from I0 to I3
  They are integer instructions with 1-cycle latency
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+

## Slide 17: Cycle-1 Behavior
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
I0 and I1 are fed to the first stage.
  The operand A of I0 has been read from the RF
    I0 is executed on FU(0,0)
  I1 has not yet got dependent B, and goes through as NOP
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I0: B=A+1
I1: C=B+1
A
B

## Slide 18: Cycle-1 Behavior
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
The execution result B is fed to FU(1,1) for executing I1 in the next cycle
The instructions are fed to the next stage
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I0: B=A+1
I1: C=B+1
B
I2: D=C+1
I3: E=D+1

## Slide 19: Cycle-2 Behavior
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
  On FU(1,1), I1 is executed
    Multiple staged IXU executes instructions in the same fetch group such as I0 and I1
  I2 and I3 are fed to the first stage
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I0: B=A+1
I1: C=B+1
B
I2: D=C+1
I3: E=D+1
C

## Slide 20: Cycle-2 Behavior
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
The execution result C is fed to FU(0,1)
  C fed to FU(0,1) is for executing I2 in the next cycle
The instructions are fed to the next stage
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I0: B=A+1
I1: C=B+1
I2: D=C+1
I3: E=D+1
C
C

## Slide 21: Cycle-3 Behavior
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
On FU(0,1), I2 is executed
  Because source C was fed from I1
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I2: D=C+1
I3: E=D+1
C
D

## Slide 22: Instructions not executed in the IXU
FU
FU
FU
FU
(1, 0)
(0, 1)
(1, 1)
(0, 0)
  I3 has not yet got dependent D, and goes through as NOP
  I3 is dispatched to the OXU
B
I0 :
=
A
I1 :
I2 :
1
+
C
=
B
1
+
D
=
C
1
+
I3 :
E
=
D
1
+
I2: D=C+1
I3: E=D+1
D

## Slide 23: Instructions executed in the IXU
The bypassing increases instructions executed in the IXU
  The ratio of executed instructions
    whose operands got from the RF: 5.5%
    whose operands got through bypassing: over 50%
In general, more instructions are executed
  when the IXU has more stages
  when the distance to producer is longer
    e.g. If I3 is distant from I2, I3 is executed

## Slide 24: Behavior when executing other instruction types in IXU
Branch
  Branches are executed similarly to INT instructions
FP
  FP instructions are not executed in the IXU
  FP instructions have long latency, and it prolongs the pipeline-length of the IXU too much
Load/Store
  Load/store instructions are executed in the IXU with the arbitration of D-Cache/LSQ between the IXU and the OXU
  If the ports are not acquired, instructions go through as NOP in the IXU

## Slide 25: Topics
The basic structure and behavior of FXA
Instruction execution in the IXU
Performance and energy consumption
Evaluation

## Slide 26: Performance Improvement of FXA
The added FUs to the IXU improve performance
  The IXU does not include the multi-ported memory, FUs can be added with low energy overhead
  It virtually widens the issue-width
e.g. In our evaluation,
  Conv. OoO: executes up to 4 instructions per cycle
  FXA: executes up to 5 instructions per cycle
    3（IXU）+ 2（OXU）
    It improves IPC by 5.7%

## Slide 27: Energy Consumption of FXA
FXA reduces the energy consumption compared with the conventional OoO processors
  Increased energy consumption for the IXU: SMALL
    IXU
    RF
  Decreased energy consumption of the OXU: BIG
    Issue Queue
    LSQ

## Slide 28: The increased energy consumption for the IXU is small
In the IXU, the energy is mainly consumed by the FUs
Dynamic energy consumption is not changed significantly
  Instructions are executed once on any FUs.
  Energy consumer is moved from the OXU to the IXU
Static energy consumption is slightly increased
  The number of FUs is increased
  INT FUs are very small and it does not cause a problem

## Slide 29: The energy consumption of the RF is not changed significantly
FU
Register File
Fetch
Rename
Issue
Queue
FU
FU
Register File
IQ
Fetch
Rename
Conventional
FXA
FU
FU
FU
FU
FU
OoO Ex. Unit(OXU)
In-order Ex. Unit(IXU)
The data-path to the IXU is added, but that to the OXU is reduced
The number of the ports is same

## Slide 30: Energy Consumption of OXU
The energy consumption of the IQ and LSQ is reduced
Issue Queue
  1)width, 2)capacity, and 3)access num are cut in half
  The energy consumption is reduced by 86%
Load/store queue
  When store instructions are executed in the IXU, order-violation detection is omitted
  Store instructions are executed in-order to successor-load instructions in the IXU, and order violation must not occur

## Slide 31: Topics
The basic structure and behavior of FXA
Instruction execution in the IXU
Performance and energy consumption
Evaluation

## Slide 32: Evaluation Environment
IPC
  In-house cycle accurate simulator
Energy Consumption
  McPAT (22nm tech.)
Benchmark programs
  All 29 programs in SPECCPU 2006
Processor Configurations
  Major micro-architectural parameters are based on ARM Cortex-A57/A53 (big.LITTLE)

## Slide 33: Evaluation Models
  BIG：
    Baseline OoO processor based on Cortex-A57
  HALF：
    In BIG, its issue width and IQ capacity are cut in half
  LITTLE：
    In-order processor based on Cortex-A53
  BIG+FX：
    FXA with the OXU of the BIG model
  HALF+FX：
    FXA with the OXU of the HALF model
    The IXU has 3 stages

## Slide 34: Baseline Configuration
  In the FXA models, the IXU is added to BIG and HALF
 | BIG | HALF | LITTLE
type | out-of-order | ← | in-order
fetch width | 3 inst. | ← | 2 inst.
issue width | 4 inst. | 2 inst. | 2 inst.
IQ | 64 entries | 32 entries | N/A
ROB | 128 entries | ← | N/A
functional unit | int:2, fp:2, mem:2 | ← | int:2, fp:1, mem:1
L1 I-Cache | 48 KB, 3 cycles | ← | ←
L1 D-Cache | 32 KB, 3 cycles | ← | ←
L2 Cache | 512 KB, 10 cycles | ← | ←
main memory | 200 cycles | ← | ←

## Slide 35: Relative Performance/Energy Ratio （The inverse of EDP） All PERs are normalized by that of BIG
HALF+FX improves the PER by 25% compared with BIG
  Because HALF+FX improves the performance and reduces the energy consumption

## Slide 36: Relative IPC in SPECCPU 2006 All IPCs are normalized by those of BIG
HALF+FX improves the IPC by 5.7%
  The IXU can execute over 50% of instructions

## Slide 37: Relative IPC in SPECCPU 2006 All IPCs are normalized by those of BIG
  In HALF, IPC is degraded by 16%
    The issue width and IQ capacity are cut in half
  HALF+FX has the OXU of HALF, but it improves the IPC significantly

## Slide 38: Relative IPC in SPECCPU 2006 All IPCs are normalized by those of BIG
BIG+FX and HALF+FX show similar IPCs
  The IXU in BIG+FX executes sufficient instructions
  The shrunk OXU in HALF+FX does not affect the performance

## Slide 39: Relative energy consumption All Energies are normalized by that of BIG
Compared with BIG, HALF+FX reduces the energy consumption by 17%
  The energy consumption of the IQ and LSQ is reduced by 86% and 23%, respectively
  HALF+FX improves the IPC, so the static energy consumption is reduced
  The increased energy consumption for the IXU is negligible

## Slide 40: Relative circuit area All areas are normalized by that of BIG
Compared with BIG, HALF+FX increases the area by 2.7%,
  Because the IXU is added
  The IXU is significantly smaller than the whole processor

## Slide 41: Executed instructions rate in the IXU while varying the FUs depth
  The execution rate increases with the increase in the depth
    The increase is saturated at 4-stage
  The FXA models were evaluated with the 3-stage IXU
    for mitigating the complexity of bypassing
    The 3-stage IXU executes 54% instructions

## Slide 42: Conclusion
OoO processors are fast, but their energy efficiency is low
We propose Front-end Execution Architecture (FXA)
  For improving the energy efficiency of OoO processors
  Add the IXU that executes instructions in-order in the front-end
    The multiple-staged IXU can execute and filter over 50% instructions with high efficiency
  Shrinks the OXU and reduces the energy consumption
Compared with Cortex A-57 (big), FXA achieves
  5.7% higher IPC and 17% lower energy consumption
  25% higher performance energy ratio(=the inverse of EDP)